## Slide 1
Clock buffering on wires
Long wires lose slew; CTS inserts buffers along the tree
learn_clock_tree — 01 clock buffering
Notes: Long wires lose slew; CTS inserts buffers along the tree.

## Slide 2
The idea
If an edge longer than maxWireLen
Buffered latency adds bufferDelay per buffer on the path
learn_clock_tree — 01 clock buffering
Notes: If an edge longer than maxWireLen, split it into equal pieces and place a buffer at each joint. Buffered latency adds bufferDelay per buffer on the path.

## Slide 3
Long wires
Long wires
learn_clock_tree — 01 clock buffering
Notes: Split edges longer than maxWireLen; place buffer squares at joints.

## Slide 4
Before buffers
Before buffers
learn_clock_tree — 01 clock buffering
Notes: H-tree may have long Manhattan legs.

## Slide 5
After insert
After insert
learn_clock_tree — 01 clock buffering
Notes: Insert buffers — joints appear on long segments.

## Slide 6
Buffered latency
Buffered latency
learn_clock_tree — 01 clock buffering
Notes: bufferedLatencies adds bufferDelay per buffer on the path.

## Slide 7
Trade-off
Trade-off
learn_clock_tree — 01 clock buffering
Notes: Buffers restore slew but add delay — skew may rise or fall.

## Slide 8
Browser lab track
Browser lab starter
learn_clock_tree — 01 clock buffering
Notes: Open **clock-buffering**. Build H-tree, click Insert buffers, count orange squares. Read buffered latencies for A.

## Slide 9
Implement track
Call `insert_buffers(edge, max_span, buffer_delay)`
Assert max segment length ≤ max_span
learn_clock_tree — 01 clock buffering
Notes: Call `insert_buffers(edge, max_span, buffer_delay)`. Assert max segment length ≤ max_span.

## Slide 10
Pitfalls
Buffering without splitting edges
Counting buffer delay twice
Using max span zero
learn_clock_tree — 01 clock buffering
Notes: Buffering without splitting edges. Counting buffer delay twice. Using max span zero.

## Slide 11
Your turn
Next: meet a skew bound with buffers and topology choice
learn_clock_tree — 01 clock buffering
Notes: Next: meet a skew bound with buffers and topology choice.