## Slide 1
Don't-care
Real specs have don't-cares , CEC must only compare care inputs, not illegal or unconstrained bits
learn_equivalence — 01 dont care
Notes: Real specs have don't-cares — CEC must only compare care inputs, not illegal or unconstrained bits.

## Slide 2
The idea
Dont_care_mask with c fixed to 0 still finds a=1,b=1,c=0 mismatch on impl_bad
learn_equivalence — 01 dont care
Notes: dont_care_mask with c fixed to 0 still finds a=1,b=1,c=0 mismatch on impl_bad.

## Slide 3
Care mask
Care mask
learn_equivalence — 01 dont care
Notes: Don't-cares mark PIs as X (−1) or fixed 0/1.

## Slide 4
Fix c=0
Fix c=0
learn_equivalence — 01 dont care
Notes: Mask with c fixed to 0 still catches the bad cex.

## Slide 5
Fewer rows
Fewer rows
learn_equivalence — 01 dont care
Notes: Fixed bits shrink the checked assignment set.

## Slide 6
X means ignore
X means ignore
learn_equivalence — 01 dont care
Notes: X on a bit means both 0/1 are allowed for that PI.

## Slide 7
Real DC
Real DC
learn_equivalence — 01 dont care
Notes: Synthesis don't-cares feed CEC care sets in industrial flows.

## Slide 8
Browser lab track
Browser lab starter
learn_equivalence — 01 dont care
Notes: Open **dont-care**. Set c care=0; run masked CEC; read reduced row count.

## Slide 9
Implement track
Call dont_care_mask(spec, impl_bad, {'a':-1,'b':-1,'c':0})
learn_equivalence — 01 dont care
Notes: Call dont_care_mask(spec, impl_bad, {'a':-1,'b':-1,'c':0}).

## Slide 10
Pitfalls
Treating X as 0
Checking illegal input combinations as failures
learn_equivalence — 01 dont care
Notes: Treating X as 0. Checking illegal input combinations as failures.

## Slide 11
Your turn
Next: sequential unrolling
learn_equivalence — 01 dont care
Notes: Next: sequential unrolling.